Group 2 Project: SHA-1 Implementation on a SoC FPGA

###### Appendix A - Simulation

Software simulation was done on a Gnome Desktop, Red Hat, Linux system running Xilinx version 14.6 ISE and ModelSIM. To launch the simulation use an emulator in bash mode and browse to the pcores/glue_v1_00_a/devl/projnav folder in the files provided. From here source the setup.sh file and then launch the ISE with the command ise glue.xise
You should have a screen as shown below [Figure A-1]:

Figure A-1: ISE Project Explorer
Verify all items are listed and have no conflicts.
To run the simulation and observe results select the simulation radio button and highlight the source labeled user_logic_tb - rtl (user_logic_tb.vhd) [Figure A-2]. Then double-click the Simulate Behavioral Model in the Processes listing

Figure A-2: Running Simulation
Here the simulation will run and give the signal wave results similar to this [Figure A-3]:

Figure A-3: Initial Waveform
This waveform will have the initial setup of the architecture as well as all four tests . It runs for a total of 3 microseconds and contains all data registers and signals. The IP bus sends data back and forth from the micro to the FPGA doing the SHA1 encryption, current_test tracks the test being run at any given time -1, and the current_state under each test label signals where in the state machine the current test is. The user_logic maintains the local micro signals and registers with data being written for each test to the slv_reg9 through slv_reg25 registers. The resulting hash calculation is written to registers slv_reg4_h0 through slv_reg8_h4 and compared to the independently calculated hash to verify correctness. The independently calculated hash was done using the Linux command-line tool ‘sha1sum’.
Once the hash is validated the simulation starts the next test and resets the micro.

Figure A-4: Test State Signals

Figure A-5: Registers
Measurements for process time were taken at the test state transitions for metrics. Some tests revisited a state and the time for both periods were added together for the data sets. [Table A-1]

	Test 1	Test 2	Test 3	Test 4
Test Type	Word Write	Single Chunk (4bit)	Single Chunk(6bit)x2	Multi-Chunk (6bit)
String Length (Bytes)	4	44	44	88
Process Start (ns)	101	119	677	1611
Process End (ns)	118	676	1610	2476
Process Length (ns)	17	557	933	865
Process Length (ns)/ 4 Bytes	17	50.64	42.41	39.32
Bandwidth (MB/s)	235.29	78.99	94.32	101.73
Reset start (ns)		120	678	1612
Rest end (ns)		129	687	1621
Reset Length (ns)		9	9	9
% Process time		1.62	0.96	1.04
Start write (ns)	101	129	687	1621
End write (ns)	109	385	943	1877
Start write (ns)(2)			1241	1927
End write (ns)(2)			1497	2183
Write Length (ns)	8	256	512	512
Write Length (ns)/ 4 Bytes	8	23.27	46.55	23.27
% Process time	47.06	45.96	54.88	59.19
Begin hash (ns)		385	943	1877
End hash (ns)		579	1137	1927
Begin hash (ns)(2)			1497	2183
End hash (ns)(2)			1513	2379
Hash Length (ns)		194	210	246
Hash Length (ns)/ 4 Bytes		17.64	19.09	22.36
% Process time		34.83	22.51	28.44
Start validate (ns)	109	587	1145	2387
End validate (ns)	117	675	1233	2475
Start validate (ns)(2)			1521
End validate (ns)(2)			1609
Validate Length (ns)	8	88	176	88
Validate Length (ns)/ 4 Bytes	8	8	16	4
% Process time	47.06	15.80	18.86	10.17
Added overhead/4 Bytes (ns)	0.000	33.636	25.409	22.318
% increase process time	0	198	149	131

Table A-1: Metric Data Analysis
###### Appendix B - Chipscope

The initial chipscope setup involve connecting the JTAG to the target hardware and scanning for chipscope monitors. In this case we have a AXI bus monitor added to our design.

Figure B-1 : Chipscope signal setup

The cdc file referenced in Figure B-1 is provided in the <git repo>/chipscope/ folder. A .cpj file is also checked in with the cdc and includes the signal renaming captured in the other screenshots.

Figure B-2 : Chipscope trigger setup on read valid signal

The first step after scanning the bus and loading the signal names, is to configure the trigger signals (Figure B-2). To capture our start scenario the read valid worked to trigger on the initial software read of the userlogic status register.

Figure B-3: Post analysis software

For any post signal analysis we used wavevcd viewer (
http://www.iss-us.com/wavevcd/Wave_msi.zip). The vcd files are included in our project submission/chipscope or <git repo>/chipscope folder. Figure B-3 shows the initial software status read and then the write of 64bytes (a block) of msg data to be hashed. Another view of the same sequence (in chipscope) is found in Figure B-4. The spacing between blocks was larger than our chipscope window so the end of the hash sequence was captured in another sequence (Figure B-5).

Figure B-4: Chipscope trigger on start of a new hash msg

Figure B-5: Chipscope trigger on the end of a hash sequence when hash is ready

The end of a data msg hash sequence results in the software waiting for a status signaling hash complete. This is shown in Figure B-5 where the trigger was a read value of 0x7 signaling the software should start reading out the hash value (5 words).

In all the chipscope captures it’s fairly obvious that the amount of bus time the software spends checking status could definitely be optimized by utilizing interrupts to request the software to read status when there’s a update/change.
###### Appendix C - Extra Reference Material

Figure C-1: SHA1 State Machine

Figure C-1 describes the overall operation of SHA1 PL design. All flow starts from the (top) userspace application running on the ARM. The boxes in green are the kernel function calls that implement the custom SHA1 interfacing to the PL (sha1_update/final as discussed in Section: “PL SHA1 Interface Module”). The boxes in yellow are interactions with the PL register map (FSM). The boxes in red are return/final states. Bringing this all together, the diagram shows the software control access and PL status interactions, as well as the data load and hash retrieval steps.

Address	Name	Reset Value	Notes
0x7AA00000	ZYNQ_SHA1_RST	0x0	Controls: start has of new msg (0x2), continue current hash(0x1)
0x7AA00004	ZYNQ_SHA1_STATUS	0x0	Status of userlogic FSM: ready for data input (0x1), Hash ready (0x2), hash busy (0x4)
0x7AA00010	ZYNQ_SHA1_H0	0x0	First word of 20 byte hash
0x7AA00014	ZYNQ_SHA1_H1	0x0
0x7AA00018	ZYNQ_SHA1_H2	0x0
0x7AA0001C	ZYNQ_SHA1_H3	0x0
0x7AA00020	ZYNQ_SHA1_H4	0x0	Last work of 20byte hash
0x7AA00024	ZYNQ_SHA1_D0	0x0	First word of 64byte block
0x7AA00028	ZYNQ_SHA1_D1	0x0
0x7AA0002C	ZYNQ_SHA1_D2	0x0
0x7AA00030	ZYNQ_SHA1_D3	0x0
0x7AA00034	ZYNQ_SHA1_D4	0x0
0x7AA00038	ZYNQ_SHA1_D5	0x0
0x7AA0003C	ZYNQ_SHA1_D6	0x0
0x7AA00040	ZYNQ_SHA1_D7	0x0
0x7AA00044	ZYNQ_SHA1_D8	0x0
0x7AA00048	ZYNQ_SHA1_D9	0x0
0x7AA0004C	ZYNQ_SHA1_D10	0x0
0x7AA00050	ZYNQ_SHA1_D11	0x0
0x7AA00054	ZYNQ_SHA1_D12	0x0
0x7AA00058	ZYNQ_SHA1_D13	0x0
0x7AA0005C	ZYNQ_SHA1_D14	0x0
0x7AA00060	ZYNQ_SHA1_D15	0x0	Last word of 64byte block

Table C-1: Control/status/data registers

Resource Links:

Notes on SHA1 - Overview of padding and tail format
http://www.itl.nist.gov/fipspubs/fip180-1.htm

Crypto dev sha testing example
http://lists.freebsd.org/pipermail/freebsd-security/2013-August/007115.html

Notes on using cryptodev-linux
https://github.com/nmav/cryptodev-linux/blob/master/INSTALL

Notes on zynq fabric loading
http://xlnx.lithium.com/t5/Embedded-Linux/download-bitfile-to-dev-xdevcfg-timeout/m-p/322419#M6137
http://forums.xilinx.com/t5/Embedded-Linux/Zynq-Loading-bitfile-into-FPGA-from-Linux-xdevcfg/td-p/237850/page/3